MZ Language

MZ is a Z80 based FORTH derivative. The main problem with FORTH on a Z80 is the twin stacks ; a Z80 only has one stack, the return stack, so much of the work has to be done by one of the other registers which move data in 8 bits.

MZ solves this problem by replacing a stack with three 16 bit registers, known as A, B and C. These registers directly map (currently) to HL, DE and BC.

The MZ language consists of words like FORTH. Unlike FORTH, every word is treated identically, though they do not of course behave identically.

MZ code is simply a sequence of MZ words, or decimal constants, or string constants

The decimal and string constants are put on the ‘stack’ using the sequence ex de,hl ; ld hl,<constant>. For strings, the value put is a pointer to an ASCIIZ string.

Words

Words are straight Z80 code, ending in a RET (or sometimes a JP rather than a CALL/RET etc.). Their functionality is defined by the lower 4 bits in the type byte in the dictionary.

Words can be marked as private. This means that they are not added to the internal dictionary at the end of a module compilation.

Words can be marked as protected. This means they cannot be executed by the user typing in to the console, because they’d probably crash it – these are words that manipulate the return stack.

Standard Words (type 0)

Standard words are normal Z80 code. To execute a word, you call it. To compile a word, you compile a call to it ; this is either a CD xx xx Z80 call, or a call that involves a page switch.

Immediate words (type 15)

Immediate words are like FORTH, they execute whether they are compiled or interpreted. They are used for words that are run on the fly, such as “if” “begin” “private” and “variable”. In the Python based compiler there are no immediate words in the dictionary ; these words are hard coded into the compiler (because you’d have to write a Z80 emulator…..).

Variable words (type 14)

Variable words convert the address to a constant (see constants), so the effect of the code is to put the current address into A (and do A→B first). Variables are private by default as they can only be accessed by routines in their own page of memory. This requires a style of code where variables are local to their module and accessor/mutator functions are used to access them from elsewhere.

Code Copying words (type 1-10)

Code copying words are an optimisation. For speed reasons, and sometimes for space reasons, and sometimes for both, code can be ‘inlined’. A code copying word consists of a number of bytes, which is the same length as the type number followed by a ret. The ret is so the code copying word can actually just be normally executed as for standard words, (subject to the protected flag)

e.g. + would be type 1 and would look like this

add	hl,de	; this one byte is the actual code.
ret	; this ret is present so it can be executed

The user cannot create these (or to be precise, isn’t allowed to). They can assumed to be in unpaged memory, so do not have to be read using far memory access.
Constants

Besides words, the language contains constants, which are decimal integers, possibly prefixed with a ‘-’. These produce code that load a constant.

When you load a constant into the register set it always goes in A, but before it does that, it transfers the contents of A into B. So constant 3 actually generates this code

ex	de,hl	; transfer A->B
ld	hl,3	; load 3 into A.

The reason for this oddity is that it allows the fluency of FORTH, MZ’s parent language. You can write , as you can in FORTH.

count @ 2 * 3 + count !

and it will work just the same (though MZ can do it better). Where it falls apart is when you need to use three values ; because then you have to use C or the return stack as a working space. (words like a>b b>c r>c exist for this purpose).

When I first conceived of this I thought it likely it would lead to an explosion of variables, but actually it doesn’t, though there are certainly more variables.

This technique sounds inherently dumb, but it actually works quite well at a slight cost in space and speed for readability. A previous version replaced the ex de,hl with a function which did the same thing when required, and the readability of the code went down significantly.

There are also string constants ; these begin with a “ mark. They put a constant (as above) which points to an ASCIIZ representation of the rest of the word, with any underscores replaced by spaces.

Dictionary

Offset	Contents
+0	Offset to next entry, normally word length + 5, 0 at end
+1	Page number of word
+2,+3	Address of word
+4	Type (0..3) Private (7) Protected (6)
+5	First character of word name (ASCII)
+n	Last character of word name (ASCII) bit 7 is set

Core Words

Word	Com?	Pro?	Description
-			B – A → A
;		Yes	Return from subroutine
: <name>	Yes		Define a word.
!			16 bit write B to memory locations A,A+1
!! @@	Yes		Variable operators
.hex			Print word on console
[-]if .. then	Yes		Conditional execution
@			16 bit read of A → A
*			A * B → A
/			B / A → A
+			A + B → A
+!			Add B into memory at A,A+1
< = > <> >= <=			Comparison B vs A → A = -1 if true, - if false
0-			2’s complement A
0<			A is -1 if A <0, 0 otherwise
0=			A is -1 if A == 0, 0 otherwise
1+ 1- 2+ 2-			Increment/Decrement A
2* 4* 8* 16* 256*			Shift A left
2/ 4/ 16/ 256/			Arithmetic Shift A right
a>b b>a b>c etc			Register→Register transfer
a>r abc> b>r c>r		Yes	Push one or all registers on stack
abs			|A| → A
and			A & B → A
begin .. [-]until	Yes		Conditional loop
begin .. again	Yes		Unconditional loop
break		Yes	Compile a Cspect break
bswap			Swap upper/lower bytes of A
c!			Save B at memory location A (8 bits)
c@			Load A from memory location A (8 bits)
copy			Move C bytes from B to A, copes with overlap.
debug			Display ABC on console
fill			Fill C bytes of memory with B starting at A
for .. next	Yes		Loop repeated a constant number of times. Note, 5 for next counts 4,3,2,1,0 and index in A at the start of every loop.
halt		Yes	Stop Z80 working
i	Yes		Get loop index into A, A → B
inkey			Read current pressed key or 0 if none
io.write.char			Print character E in colour D (Spectrum colours) at position HL
screen.mode.48k / screen.mode.layer2 / screen.mode.lowres			Set Display Mode, Clear Display
max			Larger of A,B → A
min			Smaller of A,B → A
mod			Remainder of B / A → A
module / endmodule	Yes		Brackets module code. All it does is throw an error if the module starts and ends in a different page of memory.
not			One’s complement A
or			A | B → A
p!			Write B to port A (16 bit address)
p@			Read A from port A (16 bit address)
private	Yes		Mark last definition as private
protected	Yes		Mark last definition as protected
r>a r>abc r>b r>c		Yes	Pop one or all registers off the stack.
swap			Swap A and B
sys.info			System Information address → A, A → B
variable	Yes		Make last definition a variable accessed via && !! and @@
xor			A ^ B → A